## Slide 1
PC26 · OBJECTIVE 1.1D
Shah Field
De-Bottlenecking
Quantified opportunity catalogue — surface,
subsurface & water injection
TotalEnergies ALSG × ADNOC Onshore
Asset Lead FP: Andrey Semenov
Issued 2026-04-23
CURRENT
75,733
BOPD actual
POTENTIAL
+10–12k
BOPD realistic 2026
OPPS
8
de-bottlenecking initiatives

## Slide 2
OVERVIEW
Executive Summary
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
02 / 12
CURRENT FAR
75,733
BOPD actual
2026 POTENTIAL
+10–12k
BOPD realistic
OPPORTUNITIES
8
5 subsurface · 2 surface · 1 cross-cut
DATA GAPS
9
FCT report + IPM model top of list
KEY FINDINGS
SUBSURFACE
• ~32 strings flagged "Low PIP / stim required" by RM; 1.1C only covers 5
• 12 wells rate-capped to keep BHFP ≥ Pb+100 — drawdown headroom
• Inter-reservoir water loss confirmed on 139-SS & 145-SS
• R1 under-injected ~5 kbwpd vs sustainable VRR
SURFACE
• 22 strings ESP-limited not reservoir-limited (VSD-required)
• 14 strings already at 55–60 Hz — ESP upsize candidates
• Surface back-pressure: 10 psi separator reduction ≈ +800 BOPD
• FCT report pending — biggest tractable upside still unsized
WATER INJECTION
• SY-175 & SY-180 stranded (16 kbwpd capacity) — WO in plan
• Currently 53 / 71 kbwpd vs technical rate
• Cluster #2 hard cap 25/26 Mbwpd binds Phase 2
• 12 high-WC producers cycle ~40 kbwpd of PW for ~960 BOPD

## Slide 3
BASELINE
Field Baseline — Q2-2026 Allowable
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
03 / 12
OIL PRODUCTION (BOPD)
Chart: 
| FAR (actual) | Allowable | TR | Allow incl. inactive | Ceiling
BOPD | 75733 | 76671 | 79983 | 80591 | 102752
WATER INJECTION (bwpd)
Scenario | Cluster #1 | Cluster #2 | Total | Actual
With SY-175 + 180 | 26,000 | 24,600 | 50,600 | —
Without SY-175/180 | 26,000 | 19,000 | 45,000 | 53,000
Technical rate | 42,200 | 28,800 | 71,000 | —
Cluster physical cap | 26,000 | 25,000 | hard cap | —
BASELINE READ Gap vs TR is 4,250 BOPD (5.6 %). Bigger prize sits between Allowable and the deliverability ceiling of ~102,752 BOPD, which represents the sum of estimated max rates for all active strings — and is unlocked only by capacity uplifts in subsurface and surface infrastructure. WI under-delivery (53 / 71 kbwpd vs technical rate) is the single biggest binding constraint at sector level.

## Slide 4
CLASSIFICATION
Bottleneck Map — 9 root-cause categories
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
04 / 12
BOTTOM-UP FROM RM COMMENT COLUMN
SUBSURFACE
S1
Low PIP / stim candidate
32 wells
12,000 BOPD
S2
High water cut (>60 %)
38 wells
7,000 BOPD
S3
Low BHFP — Pb risk
12 wells
1,800 BOPD
S4
Inactive — WO backlog
14 wells
3,920 BOPD
S5
Reservoir P depletion
8 wells
5,000 BOPD
SURFACE / COMPLETION
C1
Low DP / VSD required
22 wells
6,500 BOPD
C2
ESP at max frequency
14 wells
3,500 BOPD
C3
Back-pressure (flowline)
TBD
~2–4 kBOPD est.
WATER INJECTION
W1
Cluster cap 26 Mbwpd
—
physical ceiling
W2
WI integrity 175/180
2 wells
16 kbwpd stranded
W3
R1↔R2 water loss
2 wells
tracer needed
W4
High-WC producers
12 wells
PW loading
Note: Counts and BOPD-lost figures are RM-classified analytical estimates (§ANALYSIS BLOCK). C3 surface back-pressure pending Jan-2026 FCT report.

## Slide 5
PRIORITIZATION
Consolidated Ranking & Gain Bridge
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
05 / 12
RANKED BY 2026 REALISTIC GAIN
# | ID | Opportunity | 2026 BOPD | Conf. | Capex
1 | §4.5 | WI capacity (SY-175/180 + cluster) | 2,500–4,000 | M-H | $2–28M
2 | §4.7 | Surface back-pressure optimization | 1,500–2,500 | M | $0.2–8M
3 | §4.6 | PW redistribution + R1/R2 rebalance | 2,000–2,400 | M | $0.5–1.5M
4 | §4.1 | Stimulation roll-out beyond 1.1C | 2,500 | M | $8–12M
5 | §4.3 | VSD / PWS retrofit campaign | 1,600 | H | $2.4–4.8M
6 | §4.4 | ESP upsize (piggyback WOs) | 800 | M | $2.0–3.2M
7 | §4.2 | BHFP rate-cap relaxation | 900 | M-H | $0.2–0.5M
8 | §4.8 | Inactive-string reactivation | 1,000 | H | $0.5–1.0M
TOTAL realistic envelope (×0.75 overlap deduction)
~9,600 BOPD
GAIN BRIDGE — 75,733 → ~87,000 BOPD
Chart: 
| Start | §4.5 | §4.7 | §4.6 | §4.1 | §4.3 | §4.4 | §4.2 | §4.8 | Target
base | 0 | 75733 | 78233 | 79733 | 81733 | 83608 | 84808 | 85408 | 86308 | 0
value | 75733 | 2500 | 1500 | 2000 | 1875 | 1200 | 600 | 900 | 1000 | 87308
+11,575 BOPD cumulative — within 10–12 kBOPD realistic envelope. §4.1+§4.3+§4.4 deflated ×0.75 for overlap.
Saih Rawl Shuaiba analog (SPE 68222): +6,300 BOPD on smaller system via WI rebalancing + automation — directly supports the §4.5/§4.6/§4.7 envelope.

## Slide 6
OPPORTUNITY DEEP-DIVE
§4.5 — WI capacity uplift (SY-175 + SY-180 + cluster review)
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
06 / 12
2026 REALISTIC GAIN
2,500–4,000
BOPD
FULL POTENTIAL
4,000–5,500
BOPD
CAPEX BRACKET
$2–28M
$M · Med-High
MECHANISM
Phase 1 (Q2/Q3-2026): Complete WO on SY-175 & SY-180 to recover 16,000 bwpd stranded capacity. RM-mandated prerequisite: FCT in Cluster #2 / SY-148 WS before SY-180 commissioning to confirm Cluster #2 can handle the additional load (currently 19/28.8 kbwpd).
Phase 2 (2027): Cluster #2 capacity uplift study — if FCT confirms hard ceiling at 26 Mbwpd, evaluate pump/manifold capacity to lift to 35 Mbwpd.
Phase 3 (long-term): New WI well drilling if VRR confirms additional voidage to fill. Saih Rawl analog (SPE 68222): ~12 % oil rate uplift per 30 % WI rate increase.
PREREQUISITE
Cluster #2 / SY-148 WS FCT (single most important data request) · G2V2 ML#5 reservoir model · Voidage Replacement Ratio analysis
RECOMMENDATION
Approve Phase 1 SY-175/180 WO execution immediately (capex already in plan). Commission FCT in CL02/SY-148 as RM-mandated prerequisite before SY-180 start-up. Stage Phase 2 cluster uplift decision pending FCT results.

## Slide 7
OPPORTUNITY DEEP-DIVE
§4.7 — Surface back-pressure optimization
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
07 / 12
2026 REALISTIC GAIN
1,500–2,500
BOPD
FULL POTENTIAL
2,300–3,300
BOPD
CAPEX BRACKET
$0.2–8M
$M · Medium
MECHANISM
Phase 1: Station header pressure setpoint review at CDS / RDS-1 / RDS-2. Each 10 psi separator reduction across 80 R1 producers ≈ +800 BOPD via reduced WHFP and improved IPR/VLP intersection.
Phase 2: Selective flowline looping on 2-3 worst segments (>200 psi/km ΔP). Phase 3: Choke-on-test vs production-choke alignment — many wells tested at higher chokes than routinely operated.
Direct evidence pending FCT, but proxy indicators (full choke + ESP at 50 Hz + rate plateau, WHFT 150-162 °F) point to downstream restriction.
PREREQUISITE
January-2026 FCT report (single most important data request after Cluster #2 FCT) · GAP/Prosper IPM model · WHIP/WHFP-vs-time per well
RECOMMENDATION
Hold quantification at pending-FCT estimate. Once FCT report lands, commission GAP/Prosper rerun with revised separator setpoints. Phase 1 is near-zero capex — pursue setpoint review as fast win.

## Slide 8
OPPORTUNITY DEEP-DIVE
§4.6 — Produced-water redistribution + R1↔R2 rebalancing
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
08 / 12
2026 REALISTIC GAIN
2,000–2,400
BOPD
FULL POTENTIAL
2,400–3,200
BOPD
CAPEX BRACKET
$0.5–1.5M
$M · Medium
MECHANISM
(a) Inter-reservoir tracer + integrity diagnosis on 139-SS and 145-SS — RM explicitly flagged R1→R2 water loss; if confirmed, cement squeeze to restore zonal isolation.
(b) Rebalance injection R1/R2: R1 currently under-injected ~5 kbwpd vs sustainable VRR. Redirect 3-5 kbwpd from R2 to R1 once Cluster #2 integrity allows.
(c) Selective shut-in of 6 worst high-WC producers (>85% WC) — collectively producing ~960 BOPD oil but consuming 40 kbwpd PW handling capacity. Net benefit: +1,200 BOPD elsewhere via better VRR.
PREREQUISITE
PW lab analysis (TDS, scaling, particulates, H₂S) · Injector PLT / CBL on 139-SS, 145-SS · G2V2 rerun with rebalanced injection
RECOMMENDATION
Greenlight low-capex tracer campaign immediately ($0.5-1.5M). Concurrent: identify the 6 high-WC shut-in candidates from the Wells table for FY-2026 decision. PW lab work is independent and can start at any time.

## Slide 9
OPPORTUNITY DEEP-DIVE
§4.1 — Stimulation roll-out beyond Obj 1.1C
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
09 / 12
2026 REALISTIC GAIN
2,500
BOPD
FULL POTENTIAL
5,000–6,000
BOPD
CAPEX BRACKET
$8–12M
$M · Medium
MECHANISM
32+ R1 strings flagged "Low intake / Low PIP / stim required" by RM. Obj 1.1C delivers stimulation on only 5 wells in 2026.
Apply proven Naphtha+HCl recipe to 8-10 additional R1 wells per year as sustained program. Target wells with PI degradation D > 30 %/yr (1.1C methodology). Average gain +150 to +400 BOPD per well, declining 30 %/yr post-job.
Full backlog of 25 incremental candidates × 250 BOPD avg ≈ +6,000 BOPD at peak if all done within 18 months. Realistic 2026 deliverable: 10 incremental wells = +2,500 BOPD.
PREREQUISITE
Per-well PI screening across 32 stim candidates (extension of 1.1C dashboard methodology)
RECOMMENDATION
Extend the Obj 1.1C dashboard with PI-degradation screening across all 32 RM-flagged candidates. Build Q3-2026 stim queue from top-D ranking. Schedule 10 wells for 2026, decision-gate the remaining 15 against 2026 results.

## Slide 10
EXECUTION PLAN
Data Gaps & Next Steps
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
10 / 12
CRITICAL DATA GAPS
01
January-2026 FCT report
§4.7 cannot move past estimate
02
GAP/Prosper IPM model
Back-pressure sensitivities
03
G2V2 reservoir model — ML#5
§4.5 oil response · §4.6 rebalancing
04
Cluster #2 / SY-148 WS FCT
RM-mandated for SY-180 commissioning
05
PIDs / PFDs / vendor sheets
CDS, RDS-1/2, WI clusters
06
Produced water lab analysis
§4.6 chemical design
07
WHIP/WHFP-vs-time per well
§4.7 flowline hypothesis
08
Injector PLT/CBL (139-SS, 145-SS)
§4.6 (a) integrity diagnosis
09
Per-well PI screening (32 candidates)
§4.1 backlog scoping
EXECUTION TIMELINE
Q2-26
SY-175/180 WO start
PW lab campaign
FCT submission
Q3-26
Tracer 139/145-SS
VSD retrofit kick-off
Tech WS sign-off
Q4-26
SY-180 commissioning
Setpoint pilot
Stim batch 1 (5 wells)
2027
Cluster #2 uplift
Stim batch 2 (5 wells)
ESP upsizes

## Slide 11
INVESTMENT VIEW
Capex vs Gain — Prioritization Matrix
Shah Field De-Bottlenecking · TotalEnergies ALSG × ADNOC Onshore · 2026-04-23
11 / 12
TOTAL CAPEX RANGE
$16–58M
across 8 opportunities
2026 GAIN MIDPOINT
~11,575
BOPD with overlap
$ / BOPD AVERAGE
$3,200
weighted across all opps
PAYBACK @ $80/bbl
< 6 mo
on top 4 opportunities
CAPEX (X) vs GAIN (Y) — bubble = $/BOPD
Chart: 
| 15 | 4.1 | 1 | 10 | 3.6 | 2.6 | 0.35 | 0.75
Y | 3250 | 2000 | 2200 | 2500 | 1600 | 800 | 900 | 1000
§4.6 (PW redistribution) and §4.2 (BHFP relaxation) sit in the sweet spot: low capex, fast gain. §4.5 has the widest capex range because Phase 2 cluster uplift is contingent on FCT.

## Slide 12
CONCLUSIONS
Shah field can lift 10–12 kBOPD within 12 months
with the right sequencing of subsurface, surface, and WI initiatives
01
BIGGEST ABSOLUTE PRIZE IS WATER INJECTION
§4.5 SY-175/180 + cluster review delivers 2.5–4 kBOPD realistic — the largest single contribution and a pre-requisite for sustained R1 pressure support. Already partially budgeted via WO plan.
02
SURFACE BACK-PRESSURE IS THE NEXT-LARGEST AND CHEAPEST WIN
§4.7 phase-1 setpoint review costs ~$0.2M and could deliver 1.5–2.5 kBOPD. But the entire envelope is hostage to the Jan-2026 FCT report and GAP/Prosper IPM model — both still missing. Single biggest data request.
03
PRODUCED-WATER REDISTRIBUTION IS A NEAR-ZERO-CAPEX OPP
§4.6 R1↔R2 rebalancing + tracer integrity diagnosis on 139-SS/145-SS delivers ~2 kBOPD at $0.5–1.5M. Lowest-friction commercial recommendation — can start before FCT report lands.
04
STIMULATION BACKLOG IS DEEPER THAN OBJ 1.1C SCOPE
~32 R1 strings flagged "Low PIP / stim required" by RM. Obj 1.1C addresses 5. Sustained program of 8-10 wells/year via Naphtha+HCl recipe builds a +6 kBOPD asset over 18 months at $8-12M capex.
05
NINE CRITICAL DATA GAPS — FCT REPORT IS #1
Until the Jan-2026 FCT report, the GAP/Prosper IPM model, and the G2V2 ML#5 forecast are received, §4.7 stays at "pending-FCT estimate" and §4.5 Phase 2 cluster uplift decision cannot be quantified.